Problem 1

Part a

For general n, the possible values of \theta :

Part b

This problem got me thinking about how I could generate a set of normalized vectors that are separated by the same angle and how familiar this was to the Gram-Schmidt procedure for finding orthonormal vectors. GS applies for the general n but with angle \theta = \frac{\pi}{2} .

The way GS works is that when you subtract out the projection of x1 onto x2 from x1, you are left with the remaining component of x1 that is perpendicular.
Problem 2
Part a

We are trying to determine which input will force all of the cars to converge to a given configuration. Based on the information given we are interested in what happens as t approaches some far along time in the future (let’s say infinity), then the equations of motion suggest:

v_{i} = 0 therefore: \dot{v} = 0 = u_{i} - 0 leads to the obvious result: u_{i} = 0 . This also leads to: \dot{y}_{i} = v_{i} = 0 and therefore after integrating: y_{i} = constant . This makes sense in context, the constant value is simply the position i. This is interesting, as this suggests that ultimately the control schemes that we are evaluating in this problem have to approach zero as t approaches infinity.

Since y_{i} = constant = i when the system converges and the desired position then, y_{i} = v_{i}t + i after integration.

Looking at the first control scheme (right looking control), we have:

u_{i} = y_{i+1} - y_{i} -1 and for n = 5:

u = \begin{bmatrix} y_{2} - y_{1} -1 \\ y_{3} - y_{2} - 1 \\ y_{4} - y_{3} -1 \\ y_{5} - y_{4 }-1 \\ -y_{5} + 5 \end{bmatrix} = \begin{bmatrix} -1 &1& 0& 0& 0 \\ 0 & -1 &1&0 &0 \\ 0 & 0 & -1 & 1 & 0 \\ 0 & 0 & 0 & -1 & 1 \\ 0 & 0 & 0 & 0 & -1 \end{bmatrix} \begin{bmatrix} y_{1}\\ y_{2}\\ y_{3}\\ y_{4}\\ y_{5} \end{bmatrix} + \begin {bmatrix} -1\\ -1\\ -1 \\ -1\\ 5 \end{bmatrix}

Looking at the second control scheme (left and right looking control), we have:

u = \begin{bmatrix} y_{2} - y_{1} -1 \\ y_{3} - y_{2} - 1 \\ y_{4} - y_{3} -1 \\ y_{5} - y_{4 }-1 \\ -y_{5} + 5 \end{bmatrix} = \begin{bmatrix} -1 &1& 0& 0& 0 \\ 0 & -1 &1&0 &0 \\ 0 & 0 & -1 & 1 & 0 \\ 0 & 0 & 0 & -1 & 1 \\ 0 & 0 & 0 & 0 & -1 \end{bmatrix} \begin{bmatrix} y_{1}\\ y_{2}\\ y_{3}\\ y_{4}\\ y_{5} \end{bmatrix} + \begin {bmatrix} -1\\ -1\\ -1 \\ -1\\ 5 \end{bmatrix}

Problem 3

In this problem we are combining the matrix exponential solution to an autonomous linear dynamical system, eigenvalue of the system, and singular value decomposition to come up with the worst-case scenario.

My approach was to first to find out what the LDS looks like when there is no input fault.

\dot{x} = Ax(t) + Bu(t)

\dot{x} = Ax(t) + B(Kx(t))

\dot{x} = (A + BK)x(t)

\dot{x} = \tilde{A}x(t)

\tilde{A} = A +BK

When the system is not in fault, it is still an autonomous linear dynamical system. The equation when it does fault is simply: \dot{x} = Ax(t) .

My next step was to look at the sigma values and eigenvalues of both \tilde{A} and A. What I was first looking for was confirmation that \tilde{A} was a decaying system and then I was curious to see what was happening when the fault occurred.

eig(\tilde{A}) = \begin{bmatrix} -0.5000 \\ -1.5000 \\ -0.5000 + 0.5000i\\ -0.5000 - 0.5000i \end{bmatrix} and eig(A) = \begin{bmatrix} 0.5000\\ 1.0000\\ 1.0000\\ 0.5000 \end{bmatrix}

We can see that \tilde{A} is acting as described in the problem. The system is being driven to zero because the the real component of the eigenvalues are all less than zero for the continuous system. There is some oscillation but that’s not as important. When the system faults, however, the eigenvalues are all real and all greater than zero. There is no decay in the system and it will eventually “blow up” as t approaches infinity.

I then looked at the sigma values of the A matrix. What I want to do is drive the system along a right sigma vector that will have the most gain. I want the maximum gain out of the fault in the system.

\varepsilon = \begin{bmatrix} 1.3660 & 0 & 0 & 0\\ 0 & 1.0000 & 0 & 0\\ 0 & 0 & 0.5000 & 0\\ 0 & 0 & 0 & 0.3660 \end{bmatrix} V^{T} = \begin{bmatrix} -0.2654 & -0.0971 & -0.6280 & -0.7251\\ 0.4714 & -0.2357 & -0.7071 & 0.4714\\ -0.6667 & -0.6667 & -0.0000 & 0.3333\\ 0.5127 & -0.7004 & 0.3251 & -0.3753\end{bmatrix}

We see that: \sigma_{max} = 1.3660. This sigma is associated with the right singular vector:

v_{max} = \begin{bmatrix} -0.2654 \\ -0.0971 \\ -0.6280 \\ -0.7251 \end{bmatrix} .

I claim that if I set the initial condition as: x(0) = v_{max} that we will have the maximum gain when the system faults. I believe this is true because the right singular vectors are sensitive to input direction. Furthermore, v_{i} that is associated with the biggest \sigma_{i} should be the most sensitive according to the theory. However, I first had to make sure that it met the constraint that ||x(0)|| \leq 1 . As it turns out, ||v_{max}|| = 1 . Of course, this makes sense since the U and V matrices of the singular value decomposition of a matrix are orthogonal so this guarantees that the vectors have unit norms. Now, my next step was to determine when the fault should occur.

To decide this, I looked to the matrix exponential. Realizing that this is a composite system, we have two A’s that we are switching between between the time interval [0,9] seconds. Since \tilde{A} is decaying over time exponentially (ignoring the oscillations for simplicity), this system can be modeled using this plot:

You can see from the above plot of e^{-z} (z is an arbitrary variable not related to the system itself) that if we run the system too long it will hit a very rapid decay that will overpower the effects of the fault. So, if we want to maximize the fault’s effects, then we must prevent the system from entering that rapid decay. Thus, I believe that the fault should occur somewhere in the middle of [0,9] seconds so that we maximize ||x(10)|| .

Here is what the solution for x looks like so far: x(t) = e^{T_{F}\tilde{A}}e^{A}e^{(10-T_{F}-1)\tilde{A}}x(0) . Based on my above hypothesis, I used MATLAB to run the system with fault times around where I believed the fault would have the greatest effect on ||x(10)|| . I also tested extreme cases to make sure my reasoning made sense. I found that T_{F} = 4.63 maximizes ||x(10)|| .

My final solution is: x(t) = e^{4.63\tilde{A}}e^{A}e^{4.37\tilde{A}}x(0) which gives me the following: ||x(10)|| = 29.9413 where x(0) = v_{max} , the right singular vector associated with \sigma_{max} = 1.366 .

Problem 4

This is a non-linear least-squares problem with the added addition of trying to estimate the position and the time that the transmission was made. We can solve this using the Gauss-Newton method (GNM).

Using GNM, I want to linearize the residual such that I have an approximate linear LS problem:

||r(X)||^{2} \approx ||A^{(k)}X-b^{k}||^{2}

Where, in this case x actually contains three entries:
X = \begin{bmatrix} x \\ \tau \end{bmatrix} = \begin{bmatrix} x_{1} \\ x_{2} \\ \tau \end{bmatrix}

The r(x) that will be minimized is as follows:
r_{i}(X) = t_{i} - \frac{1}{c}||s_{i}-x|| - \tau

The next part is finding the linear approximation of each r_{i}(X) . This comes from the following method:

r(X) \approx r(X^(k)+Dr(X^{k})(X-X^{k}) \approx r(X^(k)+Dr(X^{k})X-Dr(X^{k})X^{k}

From here we can find the least-squares approximation:
Dr(X^{k})X + r(X^{k}) - Dr(X^{k})X^{k} = A^{k}X-b^{k}

Where:
A^{k} = Dr(X^{k}) b^{k} = Dr(X^{k})X^{k}-r(X^{k})

I worked out the Jacobian derivatives on scratch paper and found:

\frac{\partial r_{i}}{\partial x_{1}} = \frac{1}{c} \frac{(s_{i1}-x_{1})}{||s_{i}-x||} \frac{\partial r_{i}}{\partial x_{2}} = \frac{1}{c} \frac{(s_{i2}-x_{2})}{||s_{i}-x||} \frac{\partial r_{i}}{\partial \tau} =-1 Dr_{i}(X)X = \frac{1}{c} \frac{(s_{i1}-x_{1})}{||s_{i}-x||}x_{1} + \frac{1}{c} \frac{(s_{i1}-x_{1})}{||s_{i}-x||}x_{2} - \tau

Putting this all together gives the following matrices that get run through the iterative GNM in MATLAB.

  b^{k} = \begin{bmatrix} \frac{1}{c} \frac{(s_{11}-x_{1}^{k})}{||s_{1}-x||}x_{1}^{k} + \frac{1}{c} \frac{(s_{12}-x_{2}^{k})}{||s_{1}-x||}x_{2}^{k} - \tau^{k} - (t_{1} - \frac{1}{c}||s_{1}-x^k|| - \tau^{k})\\ \frac{1}{c} \frac{(s_{21}-x_{1}^{k})}{||s_{2}-x||}x_{1}^{k} + \frac{1}{c} \frac{(s_{22}-x_{2}^{k})}{||s_{2}-x||}x_{2}^{k} - \tau^{k} - (t_{2} - \frac{1}{c}||s_{2}-x^k|| - \tau^k)\\ \frac{1}{c} \frac{(s_{31}-x_{1}^{k})}{||s_{3}-x||}x_{1}^{k} + \frac{1}{c} \frac{(s_{32}-x_{2}^{k})}{||s_{3}-x||}x_{2}^{k} - \tau^{k} - (t_{3} - \frac{1}{c}||s_{3}-x^k|| - \tau^k)\\ \vdots \\ \frac{1}{c} \frac{(s_{91}-x_{1}^{k})}{||s_{9}-x||}x_{1}^{k} + \frac{1}{c} \frac{(s_{92}-x_{2}^{k})}{||s_{9}-x||}x_{2}^{k} - \tau^{k} - (t_{9} - \frac{1}{c}||s_{9}-x^k|| - \tau^k)\\ \end{bmatrix}

A^{k} = \begin{bmatrix} \frac{1}{c} \frac{(s_{11}-x_{1}^{k})}{||s_{1}-x^{k}||} & \frac{1}{c} \frac{(s_{12}-x_{2}^{k})}{||s_{1}-x^{k}||} & -1\\ \frac{1}{c} \frac{(s_{21}-x_{1}^{k})}{||s_{2}-x^{k}||} & \frac{1}{c} \frac{(s_{22}-x_{2}^{k})}{||s_{2}-x^{k}||} & -1\\ \frac{1}{c} \frac{(s_{31}-x_{1}^{k})}{||s_{3}-x^{k}||} & \frac{1}{c} \frac{(s_{32}-x_{2}^{k})}{||s_{3}-x^{k}||} & -1\\ \vdots & \vdots & \vdots\\ \frac{1}{c} \frac{(s_{91}-x_{1}^{k})}{||s_{9}-x^{k}||} & \frac{1}{c} \frac{(s_{92}-x_{2}^{k})}{||s_{9}-x^{k}||} & -1\\ \end{bmatrix}

Lastly, in order to find the next X^{k+1} we must actually solve the approximate least-squares problem:

X^{k+1} = (A^{(k)T}A^{k})^{-1}A^{(k)T}b^{k} .

The problem says that we can assume the position x is somewhere in the box |x_{1}| \leq 3000 and |x_{1}| \leq 3000 , and that \tau \leq 5000 . This information informs my educated guess for X.

In order to make sure that I have arrived at the actual solution to the problem I check the following:
||r(X)||^{2} and plot the results over all iterations. If the results converge, then I’ve found an estimate for the position of the caller and the time that the call/transmission was made. Way cool. If not, my solution either did not converge of I’ve done this wrong.

As of now, the GNM is converging but there is huge error when I calculate ||r(X)||^{k} that I don’t really believe it. I’ve tried a variety of different initial guesses within the parameters given in the problem and they all return the same solution. \tau Is not less than or equal to 5000 in my solution so I know it must be wrong. The position values are within the box, but with \tau being off, this solution is not believable. I followed the steps outline in the course notes. Code is attached.

Problem 5

Part a

After some thought, it occurred to me that the fundamental equation for eigenvalues is in the form: Av_{i} = \lambda_{i} v_{i} .

Then it occurred to me that I could make this into a least-squares problem if I looked at the equation the right way. I thought about what known information we had in the problem: the measured matrix A_{meas} which contains errors and the eigenvectors that are associated with the true matrix A. What if we assume the following:

A_{meas}v_{i} = \lambda_{i}v_{i} where y = A_{meas}v_{i} and Ax = \lambda_{i}v_{i} , giving us: y=Ax .

In this case, we are solving for the least-squares approximate solution for each individual eigenvalue of the original matrix using the “y-measurements” that contain the errors from A_{meas} .

The eigenvalues are estimated then with the following equation:

\lambda_{i-ls} = (A^{T}A)^{-1}A^{T}y = (v_{i}^{T}v_{i})^{-1}v_{i}^{T}A_{meas}v_{i}

There is only minimal iteration here: we must calculate the least-squares approximate solution for each eigenvalue. So we’d run the above line n-times for n-unknown eigenvalues.

Then from here we can construct our A_ls matrix using the eigenvalue decomposition relationship:

A_{ls} = V\Lambda V^{-1} Where the V matrix’s columns are made of the known independent eigenvectors given in the problem. V-inverse is simply the matrix whose rows are the independent left eigenvectors of A. \Lambda is a matrix whose diagonals are the least-squares approximate eigenvalues of A, all other entries are zero. Using the least-squares approximate solutions for the eigenvalues, and this equation, A_ls can be constructed.

From here, the final step is to check that J is minimized. Of course, since this is being solved as a least-squares problem, the mean-square should in fact be minimized. That’s the whole point of least-squares.

Part b

I carried out my method using the data given in the problem and found J = 0.0264. This number gives me great confidence that this is in fact the estimated A matrix. The eigenvectors are the ones given in the problem. Here are the corresponding approximate eigenvalues I found and the estimated A matrix:

\lambda_{1} = 0.7500 \lambda_{2} = 1.6287 \lambda_{3} = 2.3556 A_{ls} = \begin{bmatrix} 1.7496 & 1.1058 & -0.9996\\ 0.6230 & 2.0441& -0.6230\\ -0.1906 & 0.8981 & 0.9406 \end{bmatrix} .

Code is attached.